## Slide 1: Cartographic Design

## Slide 2: Objectives of map design
Map design
  Good map design to communicate information and data clearly, accurately and economically to users having a minimum of map reading skills.
  Factors which affect the design process
    the map user's requirements,
    his/her ability and knowledge of maps,
    the complexity of the information to be mapped,
    the available methods of map reproduction and costs.
      An understanding of the natural or cultural environment being mapped is also necessary to present a balanced reproduction of that region of the world.

## Slide 3: Design principles/Objectives of map design
Graphical signs are used in map. The sensation caused by graphical symbols/signs must have to matched to data characteristics and communication objectives in order to satisfactorily portray the information requested. e.g. :
different size of circles in increasing radius will be perceived as increment in quantity or number. Increment size of circles could be used denote number of inhabitants in each ward of a particular VDC.
Different types/symbol of dashes could be used to distinguish various kinds of linear features, roads, transmission line, administrative boundary, hydrography.
Different color(hue)/texture/should be used for different land use types such as residential, commercial, forest, riverine and lake area, agricultural etc.

## Slide 4: *
While designing topographic maps, cartographer is governed by conventions such as
  Blue for water bodies
  Dark green for forest
  Red/Pink/Grey for built up area
  Yellow for agricultural area
  Brown for contour
  North at the top of the map body
But while designing thematic maps cartographer focus on information transfer by using the innate characteristics of the variation in graphic characteristics(eg shape, size, color, texture) of symbol used.
  Population density on different administrative unit
  Volume of traffic along the route of a network
  Elevation range
  Soil types
  Land use types

## Slide 5: *
Maintain visual hierarchy. Legibility considerations play vital role.
Information hierarchy should be maintained i.e. the sequence from most to least important aspect of the data to be shown.
The theme/purpose should stand out most, should be given high visual weight. Other map features than the theme is given less weight.

## Slide 6: *Map design objectives
Map reader psychology should be understood.
Map reader pre-knowledge about map reading skills should be understood.
Map use environment taken into considerations.
Psychological aspects
Physiological aspects
Subjective aspects
Conventional aspects

## Slide 7: *Map design objectives
It is important that the correct impression is gained and that it is gained with a minimum of exertion.
  To employ this essence, concept of visual isolation is maintained on the map.

## Slide 8: Factors influencing map design

## Slide 9: Steps in cartographic/map design

## Slide 10: Geospatial data analysis
Can the data be classified / grouped?
  Useful for symbol design
  Useful for layout of the legend
What are the dimensions of the features?
  Point, line, area, volume
  Choice of corresponding symbols
What are the measurement level?
  Nominal, ordinal, interval, ratio

## Slide 11: Data classification

## Slide 12: data classification Applied to land use category

## Slide 13: Translation

## Slide 14: Perception properties
Associative
  All are perceived as being equal
Selective
  All are perceived as being different, but forming groups
Ordered
  All can spontaneously be placed in an order of magnitude.
Quantitative
  All spontaneously create an impression of amount or quantities.

## Slide 15: Information type and perception property
Information | Should be represented by a visual variables with the | Perception properties
ratio |  | quantitative
interval |  | ordered
ordinal |  | ordered
Nominal |  | Associative ( +/- selective)

## Slide 16: Visual variables and their perception properties

## Slide 17: Quantitative data
Absolute quantitative data
  Observed, measured or counted numbers
Relative quantitative data
  Calculated, derived numbers

## Slide 18: Cartographic representation of ratio data
Absolute quantities should be represented by means of visual variable with a quantitative perception
Relative quantities should be represented by means of visual variable with an ordered perception property.

## Slide 19: Absolute or relative quantities, see the difference.

## Slide 20: Perception property of combined visual variable

## Slide 21: Perception property of combined visual variable

## Slide 22: Perception property of combined visual variable

## Slide 23: Perception property of combined visual variable

## Slide 24: What is the best choice of visual variable?

## Slide 25: What is the best choice of visual variable?

## Slide 26: What is the best choice of visual variable?

## Slide 27: Principles of Cartographic Design
Design approach
Visual levels ( visual hyrarchy)
Contrast and balance
Symbol categories
Basic identification elements
Emphasis
Basic proportions

## Slide 28: Principles of Cartographic Design
Concept before Compilation
  make general plan and progress to finer details.
  Hierarchy with Harmony
  Important things must look important

## Slide 29: Principles of Cartographic Design
Visual levels
  Applies to the elements within the map and arrangement of all components of map.
  Information selected to be the foreground of the product will be the most obvious to the user and must be chosen carefully to fulfill the major objectives of the map.
  Supporting information should be treated as background material and given a lower visual level by decreased size, colour intensity, contrast and, therefore, decreased overall importance.

## Slide 30: Visual hirarchy

## Slide 31: Principles of Cartographic Design
Contrast and balance
  As a general rule, the initial design should employ the minimum degree of contrast needed to ensure that all symbols are readable and that dominant symbols appear as such.

## Slide 32: Principles of Cartographic Design
Symbol categories
  On all maps the subject matter should be organized and displayed in categories of similar items.
  Subdivisions of any one category should be shown by symbols representative of their relative importance within the category.

## Slide 33: Principles of Cartographic Design
Basic identification elements
  Basic identification elements should be clearly differentiated by the use of colour, tone or pattern over either surface.

## Slide 34: Principles of Cartographic Design
Emphasis
  Emphasis should be given to most interesting or most crucial features which are often relatively small in comparison to the total map area.

## Slide 35: Principles of Cartographic Design
Basic proportions
  The surface area used for the map face (the area within the neat lines) should be visually dominant.
  A good rule of thumb is to keep the map area to about 2/3 of the total area, with the remaining 1/3 for notes, surround, etc.

## Slide 36: In conclusion……
Design principles should be such that in produced map there must be
  Simplicity
  Clarity
  Visual hirarchy

## Slide 37: Map Design Guides
Map titles and sub-titles
  should appear in the largest and/or boldest type
  should also be short in length and describe the area or subject portrayed. “Map of” and “Chart of” should be avoided.
  Sub-title ( if any ) should be smaller in lettering size and weight than the main title.

## Slide 38
Key plan or location map
  The primary map area must be outlined and labelled for ease of recognition within the location map to locate the map area geographically in relation to a larger context.

## Slide 39
Bar scales
  The subdivision should be smaller, exact, convenient units which are appropriate for the scale and map use.
  Scales should be neither too long nor too bold to avoid dominating the map.

## Slide 40
Legend
  The symbol should be on the left, and the notes explaining it to the right of the symbol.
  must be exactly as shown on the graphic, i.e. must be identical in size, shape and colour.
  Legends must be organized or ranked.
  Symbols which do not appear on a product should not be listed in the legend. For series mapping, however, cross-referencing, economics and speed of production may dictate otherwise;
  Type (lettering) used for explanations must be simple and small. The lettering size should be the smallest which can be read by people of less than average eyesight, under realistic usage conditions;
  wherever possible items should be identified or labelled on the map face rather than including them in the legend, which is a relatively inefficient communication device.

## Slide 41: Name placement
4 basic rules of name placement
  There should be no doubt as to which place a name refers
  Name should be aligned properly and arranged tidily.
  Name should appear in the biggest empty area next to the feature being mapped
  Name should never cause the obliteration of important or significant detail on the map

## Slide 42: Colour design
Psychology

## Slide 43: Balance
If map’s message is balance
  then no one colour should overbalance the picture
  unless you really want a colour to ‘stick out’

## Slide 44: Figure ground

## Slide 45: Background

## Slide 46: Contrast

## Slide 47: Size

## Slide 48: Hue and lightness

## Slide 49: More contrast

## Slide 50: Systematic use of colour

## Slide 51: More system

## Slide 52: Hue

## Slide 53: Lightness

## Slide 54: Recommendations

## Slide 55: More………

## Slide 56: Good map design
Transmits spatially related information in an optimal manner
Restricts itself to the essential substance of the available information
Removes from the map image any unnecessary and insignificant items
Guarantees desired positional precision
Applies a symbolization, which allows for spontaneous and correct association
Is clear in its statement
Obeys the agreed cartographic protocols
Is easily legible
Is aesthetically satisfying
Is efficiently producible

## Slide 57: Good and bad map design




## Slide 58: Map accuracy
Accuracy refers to the amount of distortion (or lack thereof) in the representation of features.
Six elements of map accuracy
  positional accuracy
  attribute accuracy
  resolution
  logical consistency
  currency
  Completeness
concern the individual
elements of a data set
Concern the dataset as a whole

## Slide 59
Positional accuracy
  concerns the measurement of feature locations
  Horizontal and vertical
  Can be evaluated by check points
  Knowing about the quality of database will help to decide if it is appropriate for any project.

## Slide 60
Attribute Accuracy / thematic accuracy
  concerns the measurement of the characteristics of a feature, and can be greatly affected by data classification.
  difficult to assess, but some of the same methods used to measure positional accuracy can be used, such as sampling random features.
  However, attribute accuracy can be affected by the manner in which features are represented.

## Slide 61
Resolution
  Resolution (minimum mapping unit) refers to the size of the smallest feature in a data set that can be discerned.
  Resolution and positional accuracy are related
    the positional accuracy of any object cannot be greater than the resolution of the map.
    the resolution of a data set should influence the scale at which those data are displayed.

## Slide 62
Logical consistency
  Conformity to rules
  Logical consistency refers to the relationships between data items, and whether or not the relationships make sense.
  One way to test this is to check whether any given feature has contradictory attributes. For example, suppose your database contains information about land cover, slope, and soil type. Areas with a value of “lake” for land cover should have a value of “0%” for slope, not “10%” or “20%.”

## Slide 63
Currency ( temporal accuracy)
  Up to date
  Depend on Start-date/ end-date

## Slide 64
Completeness
  Coverage, classification, verification

## Slide 65
Thank You