## Slide 1: Lettering Basics

## Slide 2
Typography is the art and technique of arranging type to make written language legible, readable, and appealing when displayed. The arrangement of type involves selecting typefaces, point size, line length, line-spacing (leading), letter-spacing (tracking), and adjusting the space within letters pairs (kerning).(Wikipedia)

## Slide 3
More rules
  The reading and quality of any map is greatly affected by the positioning of the names and lettering used upon it. When it is properly placed, the lettering will clearly identify the feature to which it refers without ambiguity.
  Linear features - are named close to, parallel to, and normally on top of the feature. Lengthy features - more than once rather than relying on excessive letter spacing;
  Lettering should not be placed in a straight line on any diagonal, unless it parallels a linear feature. It is excessively obvious and visually disruptive, interfering with the readability of the rest of the product;
  Priority rule for point object:

## Slide 4
  The naming of adjacent features at angles close to the vertical needs particular attention. Frequent changes of direction should be avoided wherever possible;
  In naming areas (lakes, estuaries, basins, mountains, counties, regions, etc.) the name is placed within the feature if at all possible. Letter spacing is often used to better indicate the extent of the feature named. Short names which apply to long areas may have to be repeated;
  Names should be placed so that they do not interrupt other map information.
  Aligning a name precisely with any point symbol should be avoided as this can often create visual confusion, especially on those maps with unfamiliar names or terminology;

## Slide 5
There must never be any doubt as to which point or feature a name refers. Names for point symbols should be placed a distance approximately equivalent to half the height of a capital letter from the symbol name.
Names should not cross one another unless no other solution is possible;
Names which must cross each other must be clearly differentiated by either the use of letter spacing or a change in the style or size of lettering that is used;
In general, use letter spacing as little as possible;
All letter-spaced names must have equal-appearing intervals or spaces, according to the visual perception of the cartographer.

## Slide 6: Lettering basics
Lower case letters are the norm and communicate more effectively than upper case letters;
Identifying land features by upright letters and water features by italic or slanted lettering has become a widespread convention.
The size and visual weight of a name should reflect the importance of that features on the map. The smallest and least important information must be easily read and reproduceable. The remaining class sizes are chosen with the subsequent smallest increment in size and weight of letter that will be clearly seen by the average reader;
Most punctuation marks are omitted from the face of a map for simplicity and to avoid confusion with other map symbols.

## Slide 7
The End