## Slide 1: Suspension Bridge

## Slide 2
Bridges for low traffic
Span (length) - as long as 3000 feet or a little more
Weight supported by cables suspended between the two towers
Cables (strong) - thousands of wires – steel galvanised (against corrosion)
Cables / strands / Lattho

## Slide 3: Construction of cable
-> Twisting the wires
-> Spinning together and clamping at intervals ( for longer bridges)

## Slide 4
Cables -> top of the towers -> to the side towers -> into the anchorage (Saddles to hold)
The ends ->fixed to the anchorage
A) Natural Rocks
B) Concrete/ mansory
Cables -> looped and fixed at the base of the anchorage

## Slide 5
Intervals -> cast steel cable bands for gripping
From bands -> suspenders hang down
Suspenders have high tensile strength
Suspenders protect the bridge from deformation of the deck
Deck -> flat part of the bridge
Deformation -> from traffic, from wind pressures
Binders/trusses are also used along the level of the deck for stiffening the bridge